## Slide 1: Carbon accounting on the goodman unit

## Slide 2: OVERVIEW
Alternatives of Goodman Unit Management
Carbon Calculations
Carbon Certification
Wood Buildings
Goodman unit area: ~7,700 hectares
Total Carbon:
1.9 million tonnes of Carbon
6 million mega grams of CO2 equivalence

## Slide 3: Alternatives of Goodman Unit Management
Hyunju Lee & Luyi Li
Notes: Straightforward & keep short (too long last week)
Make sure explain each scenario clearly
Ok. We are going to explain 3 alternative of goodman forests management.

## Slide 5: Management Scenarios:
Baseline
No Management
Sustainable Forest Management

## Slide 6: 1. Baseline
 | How much area: 1.5% of Goodman Unit
 | How often: Every 5 years
 | Treatment: Clear-cut, leave 8 (of the largest) tree/acre
 | Total rotation years: 375 years
 | Example: Clear-cut 1.5% of Goodman Unit re-harvest the same stand in the year 2394
Notes: The first alternative is the Base Line which is currently undergoing at Goodman Unit
How much area: 1.5% of Goodman Unit
Which way: clear cut but leave the largest 8 trees for habitat? Or timber???
How often: every 5 years
Therefore rotation years is 375 years. For reference, Pack forest’s rotation year is 60 years????
The stand cut in 2014 will be cut again in 2394.

## Slide 7
2014 | 2024
2034 | 2044
Stand Visualization of Baseline Management, Stand: 21153
Notes: These photos show the 1.5% forest condition of which is applied clear cut and left 8 trees/ acre. (As you can see there are 2 big trees left, so this photos show .25 acre of the 1.5% forest which is applied clearcut. )

## Slide 8: 2. No Management
 | Advantages: Maximize current carbon No costs for plans or managements
 | Disadvantages: No timber value Risk of wind damage
Notes: We choose this alternative to show you what happens if we do nothing for forest management.

## Slide 9
2014 | 2024
2034 | 2044
Stand Visualization of No Management, Stand: 21153
Notes: As you can see, the forest is getting dense as time passes. The forest has natural thinning treatment by their high dense condition, but still it has lots of small diameter trees compare to treated forests.

## Slide 10: 3. Sustainable Forest Management
 | How much area: 17% of the Goodman forests
 | How often (interval): Harvest 5-yr, PCT 10-yr
 | Which way: - Harvest 70%, Retain 30% - Re-plant 300 Douglas fir seedlings/acre - Pre-commercial thin in 10 years from harvest (e.g. 1st PCT 2024- 1*10 = 2014, 2nd 2034 - 2*10 = 2024)
*Increased investment as intensive treatment involved.
PCT = Pre-commercial Thin
Notes: - Leaving 150 TPA
Harvest 70% of the trees, Retain 30% (largest trees
Precommertial thin cut all trees 0 – 8” DBH, this will promote growth in the stand of the planted trees
Leaving 150 TPA

## Slide 11
2014 | 2024
2034 | 2044
Stand Visualization of Sustainable Forest Management, Stand: 21153
Notes: As you can see forest

## Slide 12: Carbon Calculations Shannon A. Armitage & Brooke Cassell

## Slide 13: Carbon Calculations
Landscape Management System (LMS)
Developed by University of Washington
Simulates forest growth under forest management prescriptions

## Slide 14: Carbon Calculations
Landscape Management System (LMS)
10% Random Sample
(41 stands out of 411)

## Slide 15: Carbon Calculations
Landscape Management System (LMS)
10% Random Sample
(41 stands out of 411)
  Ran many types of simulations and settled on three realistic possibilities

## Slide 16: Carbon Calculations
Landscape Management System (LMS)
10% Random Sample
(41 stands out of 411)
  Ran many types of simulations and settled on three realistic possibilities
  Projected forest growth for 30 years, which should prevent too much error from the model

## Slide 17: Carbon Calculations
Landscape Management System (LMS)
10% Random Sample
(41 stands out of 411)
  Ran many types of simulations and settled on three realistic possibilities
  Projected forest growth for 30 years, which should prevent too much error from the model
  Multiply by 10 for total unit carbon

## Slide 18: Carbon Calculations
Excel-based Carbon Calculator
(Browne, J.E. 1962)
(U.S. Forest Products Laboratory, 1974)
(Gholz, H.L. et al., 1979)
Carbon computed for trees only
Stems
Roots
Branches
Foliage
Not including soil or understory vegetation

## Slide 19: To get our baseline carbon...
ACTUAL DATA:
411 plots
18,862.79 acres
2004 ~ 277.77 acres clear cut (1.5%)
2009 ~ 270 acres clear cut (1.4%)
SIMULATED DATA:
41 plots (10%)
1,922 acres (10.2%)
2004 ~ 29.12 acres clear cut (1.5%)
2009 ~ 27.41 acres clear cut (1.4%)
Then we simulated growth to 2014

## Slide 20: Where are we now?
2009: 5,355,371 metric tons CO2e
2014: 6,140,677 metric tons CO2e
Annual Uptake Rate
157,061 Mg CO2e / year

## Slide 21
Chart: Annual CO2e Uptake
| 2009 | 2014 | 2019 | 2024 | 2029 | 2034 | 2039
Baseline Harvest | 133372.1347 | 145742.966 | 126327.1422 | 115140.8373 | 134262.4552 | 118612.5222 | 122858.0151
No Management | 149969.3572 | 157061.1542 | 158415.6002 | 156151.9341 | 151880.9693 | 146187.7112 | 140257.1308
Sustainable Harvest | 133372.1347 | 118947.3288 | 111582.1406 | 83635.4171 | 62868.9644 | 92790.4453 | 128053.4426
Chart: Total CO2e in the Goodman Unit
| 2009 | 2014 | 2019 | 2024 | 2029 | 2034 | 2039
Baseline Harvest | 5272384.8985 | 6001099.7284 | 6632735.4393 | 7208439.626 | 7879751.9018 | 8472814.513 | 9087104.5887
No Management | 5355371.011 | 6140676.7819 | 6932754.7829 | 7713514.4533 | 8472919.2997 | 9203857.8556 | 9905143.5098
Sustainable Harvest | 5272384.8985 | 5867121.5426 | 6425032.2455 | 6843209.3312 | 7157554.1532 | 7621506.3795 | 8261773.5927

## Slide 22: 30 year Management Scenarios 2009 - 2039
Management Scenario | Average Annual Carbon Uptake (Mg CO2e) | Average Annual Timber Revenue | Range of Annual Timber Revenue
1. Baseline | 127,157 | $35,343 | $10,500 – $58,000
2. No Management | 151,659 | $0 | $0
3. Sustainable Forest Management | 99,646 | $28,749 | $16,000 - $57,000

## Slide 23: A Few Considerations
Our simulations were run on a theoretical, homogeneous landscape based on average conditions across the Goodman Unit.
For truly accurate predictions, each stand will need to have an individual prescription based on its proximity to streams, potential for habitat, etc...
The model does not account for the extensive natural regeneration of western hemlock that occurs on the Olympic Peninsula, so the amount of carbon is likely underestimated.

## Slide 24: Certification
Eric Snoozy & Gregg Zimmerman

## Slide 25: Introduction to 3rd Party Certification
To officially claim offsets certification must be obtained
Certification process
  Carbon Offset vs. Carbon Credit
Parties involved in certification
How to obtain forest certification

## Slide 26: Certification Standards
Several Certification Standards:
        Climate Action Reserve
        American Carbon Registry
        Climate, Community and Biodiversity Standards
        Verified Carbon Standard
        The Gold Standard

## Slide 27: Project Types
Avoided Conversion
  Stopping conversion to
    Agriculture
    Industrial
  From peat swamps
Improved Forest Management
  Increases live standing carbon in forest
  Employs natural forest management practices.
To obtain certification a “project” must be created
In our case, the “project” would be the Goodman Unit
Afforestation, Reforestation, Revegetation
  Creating new forests

## Slide 28: Hurdles to Certification on the Goodman Unit
DNR cooperation
Land title or timber rights
Provide management plan(s) that meet requirements for “Natural Forest Management”
Continued monitoring each year (for 100 years)

## Slide 29: Recommendation:
In order to count the Goodman unit as an offset it must be third party certified.
Our recommendation is to use the Climate Action Reserve certification standard. Although there are challenges to certifying this unit, certification should be considered for claiming offsets consistent with current guidelines.

## Slide 30: WOOD BUILDINGS
Matt Grund & Mikhael Kazzi

## Slide 31
Carbon Smart
Energy Efficient
Potentially Costs less
Improves LEED ratings
Efficiently Reused and Recycled
Why Wood?

## Slide 32
http://www.corrim.org/pubs/factsheets/fs_05.pdf
Wood is Carbon Smart
Requires significantly less energy to manufacture than steel and concrete
Stores enough C during lifetime to offset emissions from fossil-fuel intensive concrete
Notes: Wood helps to minimize energy consumption in several ways. In terms of embodied energy, which includes the energy required to extract, process, manufacture, transport, construct and maintain a material or product, life cycle assessment studies (LCA) show that wood significantly outperforms both steel and concrete.
Lesser known is the fact that trees incorporate the absorbed carbon (C) into their wood, and products made from that wood, such as lumber and furniture, continue to store the carbon indefinitely. Because manufacturing processes associated with wood products require less energy,they are responsible for far less greenhouse gas emissions than materials such as steel or concrete.

## Slide 33: Wood is a LEED-er
Building with wood improves LEED ratings
  Resource Locality
  Renewable Materials
  Salvaged/Reusable Materials
  Construction Waste Diversion
  Low Emitting Materials
Notes: Using wood as a primary construction material can potentially increase our LEED ratings with future buildings in the following categories. If we can harvest from the Goodman unit, we will certainly meet the resource locality standard, wood is a renewable material, there are many examples of buildings which have incorporated salvaged and reclaimed wood as a main construction material and it has proved to retain its strength, durability, and fire resilience. Wood is more efficiently recycled and reused than concrete or steel, which we will touch on a bit later, and most of the engineered wood products today contain very few VOC’s in their adhesives.

## Slide 34: Energy Efficiency and Cost
Bethel School District
All schools built with wood frames
Energy Star rating of 81%
  Several schools even achieved 95% - 98%
Wood allows over-insulation
Washington State Code
  Steel/Concrete needs thermal break between exterior and interior walls
  Thicker walls = More Cost
  Wood is exempt!!

## Slide 35: Cost and Carbon Savings
Stadthaus Complex
Costs 15% less than concrete/steel replicate
¼ the weight of concrete/steel
  Lowers transport cost
Built w/ Cross-Laminated Timber
  Significantly reduced construction process
  Stores even more C than dimensional lumber
  Positive C footprint for 20 years!

## Slide 36
Total Emissions – 24,993 Mg CO2e
  Concrete 12,375 tons
  Steel 514 tons
  Wood 688 tons (550 MBF)
95% of Lander is concrete and steel
5% of Lander is wood
Case Study: Lander Hall
Chart: Mass of Material in New Lander Hall
Contcrete + Steel | 12375 | 514
Wood | 688
Notes: Just based on the construction materials

## Slide 37: Lander Hall Carbon Emissions and Savings
naturally:wood* | 630 BF (1m3) Dimensional Lumber
Carbon Stored | +765 kg CO2e
Carbon Emissions (Harvesting, Manufacturing and Transportation) | -185 kg CO2e
Building Lifespan | Carbon Sequestered
50 years | +198 kg CO2e
75 years | +389 kg CO2e
100 years | +580 kg CO2e
Life-Cycle Assessment
  PAS 2050 protocol
  Full Carbon credit after 100 years (75% for 75yrs, 50% for 50yrs)
Lander emits..
  50yr: 24,993 Mg CO2e
  75yr: 24,826 Mg CO2e
  100yr: 24,440 Mg CO2e
All Wood-Lander offsets..
  50 yr: +2083 Mg CO2e
  75 yr: +5370 Mg CO2e
  100yr: +8655 Mg CO2e
Lander Hall | 550,000 BF Dimensional Lumber**
50 years | +173 Mg CO2e
75 years | +340 Mg CO2e
100 years | +506 Mg CO2e
*naturally:wood: Demonstrating Wood’s Carbon Benefits, Feb. 2011
**John Gilson of Walsh Construction; Troy Stahlecker of UW Capital Projects Office
Notes: So I realize there’s a lot of numbers here, but let me tell you what to pay attention to. With the current wood…
According to the acclaimed wood research center, naturally:wood, we can see that the carbon stored in 1 cu. meter of softwood lumber is more than 3 times greater than the emissions from the harvesting, manufacturing, and transportation combined. The net carbon balance is based off of a 100 year global warming potential, meaning he full carbon savings can only be achieved if the building lasts 100 years. If it lasts 75 years, it will achieve 75% of its carbon savings, and in 50 years (which is the typical lifespan of a building), the wood in the building will achieve only half of its carbon savings potential.
We used the PAS 2050 standard of a 100 year global warming potential which provide sa consistent method and process for the determination of the life cycle GHG emissions associated with specific product or products.

## Slide 38: Lander Emissions and Offsets Projections
Lander w/ 50 year lifespan is 90% wood to = Net Zero Carbon
  >90% to achieve offsets
  100 yr Lander w/ 62% wood
Increase Lifespan
  Increase C Savings
  Less wood for C offsets
Increase % Wood
  Increase C Savings
  Increase offsets in less time
Increase Lifespan and % Wood
  Largest offsets
  Most sustainable
Chart: Lander Emissions
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
50yr Lifespan | 13410.1955 | 13069.5815 | 11226.0857 | 9562.4368 | 7898.788 | 6235.1391 | 4569.5276 | 2905.5516 | 1244.1926 | -419.4563 | -2083.1051
75yr Lifespan | 13410.1955 | 12741.0094 | 10568.9415 | 8576.7206 | 6584.4996 | 4592.2787 | 2596.2018 | 603.3382 | -1384.3841 | -3376.605 | -5368.826
100yr Lifespan | 13410.1955 | 12412.4374 | 9911.7973 | 7591.0043 | 5270.2113 | 2949.4183 | 622.876 | -1698.8753 | -4012.9608 | -6333.7538 | -8654.5468
Current Lander | 13237.3384 | 13070.5923 | 12903.8463
Notes: In the purple, we see the emissions from the current Lander with 5% of the building constructed from wood at the lifespan of 50, 75, and 100 years. As we can see, age does not make too significant of a difference in emissions at the 5% wood level. But the savings differences within the life-spans are clear once Lander is built using more wood.
Carbon savings become more pronounced within lifespan as % wood increases.
Able to reach net zero emissions with less wood if buildings have a longer lifespan
The net emissions from the construction of Lander are heavily dependent on the building’s lifespan as well as the amount of wood used in construction. Since wood stores more carbon than the combined carbon in its harvesting, manufacturing, and transportation, it is entirely feasible to achieve net zero emissions on buildings, where the increased use of wood and life cycle of the building account for the carbon debt created by up the fossil-fuel intensive construction materials, namely concrete and steel. Lander can achieve net zero emissions and even carbon savings. For a Lander with a 50 year life span, which is the typical lifespan of buildings, appx. 80% of its construction must use wood, for 75 year old Lander, it must be built with 60-65% wood and for a 100 year old Lander, a little more than half of its construction must be comprised of wood.

## Slide 39: Conclusion
Alternatives of Goodman Unit Management
Carbon Calculations
Carbon Certification
Wood Buildings
Goodman unit area: ~7,700 hectares
Total Carbon:
1.9 million tonnes of Carbon
6 million mega grams of CO2 equivalence

## Slide 40
Chart: CO2e (Mg)
| Goodman Unit Carbon Sequestration | University Emissions
 | 157061 | 164350
Annual Goodman Unit Uptake & University Emissions
To Achieve Carbon Reduction of Building Materials:
  Increase Life Span
  Use Wood in Buildings

## Slide 41: Acknowledgements
We would like to thank Dr. David Ford and Dr. Greg Ettl for their assistance with this project
As well as:
  STARS
  Jeff Cominick
  Jason Cross
  Guarrin Sakagawa
  Dr. Rolf Gersonde
  Dr. Elaine Oneil
  Dr. Tom DeLuca
  Troy Stahlecker
  Walsh Construction